## Slide 1: 4th April to 8 April
Experiment start: 6:51 pm (Thursday)
First Data Point measured is at: 7:01pm
Experiment stopped at about: 1:10 pm (Monday)
Container #2

## Slide 2: List of Parameters
Air Temperature (°C)
Temperature in Substrate (°C)
Relative Humidity (%)
Moisture Content (Only Middle Container, Top & Bottom Readings are invalid)
pH Value
Methane (ppm)

## Slide 3: Fan Speed Increased to 40% on Sunday, Time: 1:31 pm

## Slide 4: Air Temperature (°C)
Fan speed maintain at 20% PWM, except for one time on Sunday, temp exceeded Threshold of 33 °C

## Slide 5: Readings at (Inlet) & (Outlet) does not appear to have large difference

## Slide 6: Temperature in Substrate(°C)
Parameter did not exceed Threshold of 36 °C

## Slide 7: Trend for Temp Readings in all 3 containers are same(?)
Temp in the Bottom Container (#1) is slightly higher than rest during the second, third and forth day.

## Slide 8: Placed Both Temperature readings on the same Graph

## Slide 9
Temperature readings display a common pattern ?

## Slide 10: Relative Humidity
Parameter did not drop below 40 %

## Slide 11
Relative Humidity is lowest when the Sun is at its peak.
Relative Humidity exhibits a decreasing trend.
(Enclosed with ventilation)

## Slide 12: Moisture Content

## Slide 13: Moisture Content in Substrate slowly decreases
Moisture Readings for Bottom and Top Containers indicates dryer moisture level… Likely sensor not place deep enough or in a location that is not in good contact with substrate

## Slide 14: pH Value

## Slide 15: Not sure why the pH value is able to spike this large
pH value does not increase gradually like experiment in phase 1

## Slide 16: Methane

## Slide 17: Methane reading has a positive upward trend (?)
Methane readings is highest after 12pm, evening (6pm) drops.
Except for 8-DOL (Sunday) and 9-DOL (Monday)